MagnoTricorder: What you Need To Do Before Leaving Home
Mostafa Uddin & Tamer Nadeem

---
Smart Devices
Surrounded By Smart Devices

---
Smart Home
Sensing the status of home devices is important to have better control
Home devices address any electric devices at home including home appliances, computing devices, non-computing devices etc.

---
Our Vision
Smart Devices
Sensing Capability
Sense Status of
the Machines
Better Control Over
Machines

---
Scenario
Did I turn off the AC at home?
PROBLEM:
Bob is on his way to lab office

---
Scenario
PROBLEM:
Leaving home appliances or devices on while you are
not at home can have severe circumstances
Home fatalities
Wasting Money

---
Scenario
SOLUTION:
Checklist Before leaving home
AC/Heating
Kitchen Stove
Kitchen Woven
Light/Lamp
PC/Laptop
Fan
OR
Bob can utilize the smartphone sensing capability to detect any on home devices/appliances from a single-point.

---
Our Solution:MagnoTricorder
- Utilize the magnetic sensor in smartphone.
- Leverages Electro Magnetic Interference of AC current in main power line.
- Detect running home devices/appliances from a single point (Circuit Breaker Panel).
- Name is inspired by StarTrek device: Tricorder.

---
MagnoTricorder: Usage
Bob can do the following on his way out home:
Action 1: He can run the MagnoTricorder application in his smartphone while he is holding it near the Circuit Breaker Panel(CBP).
Action 2: After few second MagnoTricorder will inform Bob which home device is still on.

---
Placement of CBP?
- National Electric Code (NEC) is adapted by most buildings in USA.
- NEC recommend to place CBP in a clear, easily accessible and safe place.
- In some countries CBP is placed near the entrance.
- Placing CBP near the entrance is a suitable place for single-point sensing.

---
Background
- Multi-Sensing Framework: Exploit different modalities in smartphone to build a unique fingerprint profile of a machine.
- Previously we have used sound sensing capability to build such profile for each home device.
- Problems with sound sensing:
  - Device that does not generate sound.
  - Device proximity requirement.

---
How idea evolved?
- We want to overcome the limitation of sound sensing to detect home devices.
- The flow of AC current depends on the load of running devices at home.
- Conducting AC current in main power line generate Electro Magnetic Interference(EMI).
- AC current → EMI
- EMI induce magnetic field that fluctuates magnetic sensor reading in smartphone.

---
How idea evolved?
We took the Nexus S phone near the CBP in order to collect the magnetic sensor reading.
Magnetic sensor reading from the Nexus S phone while different devices were running.

---
Some challenges
- Magnetic sensor in smartphone has very narrow bandwidth low pass filter.
- Less sensitive to high frequency (60Hz) interference.
Can we still utilize the Interference over magnetic sensor reading in smartphone to detect running home devices/appliances?

---
MagnoTricorder Framework
- Data Collection: Collect and Preprocess raw magnetic sensing data.
- Features Extraction & Selection: Extract and select both time and frequency domain features.
- Classification: Training algorithm to build a classification model, later used for texting.

---
MagnoTricorder: Data collection
- We place the Nexus S phone on the top of the CBP surface as above picture.
- We have collect the data over 3 days period of time.
- Each day we place the phone at different orientation.
- We split the collected data to two set: training and testing data.

---
MagnoTricorder: Data collection
- Collect magnetic sensor reading while no device is running.
- Over 3 day period, we collect 15-20 minutes of data for each home devices.
- We collect data for 1) Heating on 2) Heating Pause 3)Air Condition on 4) Oven on 5) microwave on 6)Light on 7)Laptop plugged in 8)All Off

---
MagnoTricorder: Feature Extraction
We have two main goals:
1) Features should be able to differentiate between different devices.
2) Selected features should not be sensitive to the smartphone's orientation
We extract both time domain and frequency domain features

---
MagnoTricorder: Data Preprocess
- Raw data preprocess:
  - Epoch: We split the magnetic sensor data samples into sequence of non-overlapped five second periods.
  - We apply feature extraction on each epoch.

---
Feature Extraction: Time Domain
- Each epoch has total 118*5= 590 sample.
- Combine the 3-axis magnetic sensor reading for each sample.
- Calculate the mean and variance for each epoch.

---
Feature Extraction: Time Domain
Highlights:
1. Calculated mean values are highly dependent on both the orientation and distance of smartphone with respect to CBP.
2. Variance values are not sensitive to the smartphone's orientation but sensitive to distance.
3. Actual position of the smartphone on CBP cover has some effects on the magnetic sensor reading.
We consider smartphone would be placed near the center of the CBP cover.

---
Feature Extraction: Frequency Domain
- Applying FFT on the samples of each epoch.
- Extract power, |FFT(x)|² values at different frequencies for different device.
- Exclude the power values at frequency 0Hz.
- Exclude the power values beyond frequency value 3.5Hz.
- We extract power values for frequency bin 2 to 65.

---
Feature Extraction: Frequency Domain
- Figure shows the power values of different devices for the frequency range 0-3.5Hz.
- Power values beyond 3.5Hz is negligible.
- Power value at 0Hz represents the DC component which is sensible to the orientation and the position of the smartphone.

---
Feature Extraction: Frequency Domain
Figure shows the power values for the 64 frequency bins (from 2 to 65) for different devices.

---
Feature Extraction: Frequency Domain
Figure shows the Inverse FFT signal of the power values when applied to the 64 frequency bin.
Each device shows a unique signal pattern

---
Feature Extraction: Features Evaluation
- We rank the potential features based on Information gain.
- We measure entropy value as a measure for Information gain with respect to training data.
- We select top ten features with highest Information gain.

---
Feature Extraction: Features Evaluation
Scatter Plot of all training data with respect to to three features: Variance, Power at frequency bin 2 and 4.

---
Training and Testing Data
We use first two days data as training data.
Third days data for testing data.
Number of epochs of the training and testing data.

---
Classification Model
- We use weka Software* to build the classification model.
- We select the training algorithm with low-complexity implementation: Bayes Network, naïve Bayes and K-nearest neighbor.
* Weka Software: http://www.cs.waikato.ac.nz/ml/weka

---
Robustness of the Selected Features
- We one days data for training and other two days data for testing.
- We use Bayes Network to build the classifier model.
T = Data is used for training
X = Data is used for testing

---
Robustness of the Selected Features
High accuracy results validates the robustness of the selected features.

---
Evaluation: Different Days/Times
- We use Bayes Network to build the classifier model.
- We use first two days data for training.
- We collect new testing data after two weeks period from the training data.
- New testing data was collected over two days.
- In first day, we collect the data from 8:00-8:30pm.
- In second day, we collect the data from 10:00-10:30am.

---
Evaluation: Different Phones
- We use Two Nexus S phones.
- One phone is used to collect training data.
- Other phone collect the testing data.
- We use Bayes Network classifier.
- We 10-fold cross validation over the testing data.
- Overall accuracy is 95% over the testing dataset.

---
Evaluation: Different Phones
Features extracted from the Heater pause event almost overlap with the features extracted from the Oven event.

---
Related Work

---
Future Work
- Detecting multiple running devices:
  - How to detect two or more devices while they are on?
- Position of the Smartphone on the CBP cover:
  - How the collected data changes with the position of the smartphone on the CBP cover?
- Evaluation different phone models:
  - How our system perform using different phone models?

---
Thank You
Email: muddin@cs.odu.edu
Web: http://www.cs.odu.edu/~muddin